## Slide 1: STM32 Dist.
Micro103

## Slide 2: Basic communication peripherals
UART (2.1)
  UART Interrupt lab (2.1.2)
  UART DMA lab (2.1.3)
SPI (2.2)
  SPI Poll lab (2.2.1)
  SPI Interrupt lab (2.2.2)
2

## Slide 3: Timing peripherals
TIM (3.2)
  TIM Interrupt lab (3.2.1)
  TIM PWM out lab (3.2.2)
3

## Slide 4: 2.1.1 UART Poll lab

## Slide 5: Simple UART communication
Objective
  Learn how to setup UART in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Work in pairs, one will create transmitter and second receiver
Goal
  Configure UART in CubeMX and Generate Code
  Learn how to send and receive data over UART without interrupts
  Verify the correct functionality
2.1.1

## Slide 6: Simple UART communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Pin selection
  We are looking for free pins where is possible to create wire loopback connection
2.1.1

## Slide 7: Simple UART communication
Pin selection
  We are looking for free pins where is possible to create wire loopback connection
Image from STM32F429-Discovery user manual
2.1.1

## Slide 8: Simple UART communication
Pin selection
  We are looking for free pins where is possible to create wire loopback connection
Image from STM32F429 datasheet
2.1.1

## Slide 9: Simple UART communication
Hardware preparation
  We connect selected pins together by jumper, this help us to create loopback on UART
Hardware connection RX <-TX
TX>RX
2.1.1

## Slide 10: Simple UART communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX UART selection
  Select USART1 in asynchronous mode
  Select PA9 and PA10 for USART1 if weren't selected
2.1.1

## Slide 11: Simple UART communication
In order to run on maximum frequency, setup clock system
Details in lab 0
2.1.1

## Slide 12: Simple UART communication
CubeMX UART configuration
  Tab>Configuration>Connectivity>USART1
2.1.1

## Slide 13: Simple UART communication
CubeMX USART configuration check:
  BaudRate
  World length
  Parity
  Stop bits
  Data direction
  Oversampling
2.1.1

## Slide 14: Simple UART communication
CubeMX USART GPIO configuration check:
  On high baud rate set the GPIO speed to HIGH
  TAB>Configuration>System> >GPIO
  Set the HIGH output speed Button OK
2.1.1

## Slide 15: Simple UART communication
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.1.1

## Slide 16: Simple UART communication
Init GPIO and NVIC for UART
HAL_UART_MspInit callback
HAL_UART_Init(&huart1);
Init UART1 structure
HAL Library init flow
Peripheral Initializations
MX_USART1_UART_Init();
1. We need init UART1
2. Call UART1 init function
3. Store UART1 configuration into structure
4. Write to UART1 registers
5. UART1 init callback
6. UART1 GPIOS, NVIC and RCC init
7. Next periph init or user code
2.1.1

## Slide 17: Simple UART communication
HAL Library transmit flow
Created by user
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
HAL_UART_Transmit/Receive
HAL_BUSY
2.1.1
Generated by CubeMX

## Slide 18: Simple UART communication
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
  Into infinite while function
For transmit use function
  HAL_UART_Transmit(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size, uint32_t Timeout)
For receive use function
  HAL_UART_Receive(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size, uint32_t Timeout);
2.1.1

## Slide 19: Simple UART communication
Transmit solution
  Create data structure for data
  Call transmit function from while loop
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_UART_Transmit(&huart1,data,10,1000);
}
/* USER CODE END 3 */
/* USER CODE BEGIN 0 */
uint8_t data[]={0,1,2,3,4,5,6,7,8,9};
/* USER CODE END 0 */
2.1.1

## Slide 20: Simple UART communication
Receive solution
  Create data structure for data
  Call transmit function from while loop
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_UART_Receive(&huart1,data,10,1000);
}
/* USER CODE END 3 */
/* USER CODE BEGIN 0 */
uint8_t data[10];
/* USER CODE END 0 */
2.1.1

## Slide 21: 2.1.2 UART Interrupt lab

## Slide 22: Use UART with interrupt
Objective
  Learn how to setup UART with interrupts in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with interrupts
Goal
  Configure UART in CubeMX and Generate Code
  Learn how to send and receive data over UART with interrupts
  Verify the correct functionality
2.1.2

## Slide 23: Use UART with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Pin selection
  It will be same as previous lab we use again PA9 and PA10
2.1.2

## Slide 24: Use UART with interrupt
Hardware preparation
  We connect selected pins together by jumper, this help us to create loopback on UART
Hardware loopback
2.1.2

## Slide 25: Use UART with interrupt
In order to run on maximum frequency, setup clock system
Details in lab 0
2.1.2

## Slide 26: Use UART with interrupt
CubeMX UART configuration
  Tab>Configuration>Connectivity>USART1
2.1.2

## Slide 27: Use UART with interrupt
CubeMX UART configuration check:
  BaudRate
  World length
  Parity
  Stop bits
  Data direction
  Oversampling
2.1.2

## Slide 28: Use UART with interrupt
CubeMX USART configuration NVIC settings
  TAB>NVIC Settings
  Enable interrupts
  OK
2.1.2

## Slide 29: Use UART with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.1.2

## Slide 30: Use UART with interrupt
HAL Library UART with IT transmit and receiev flow
Start process with interrupt generation at end of process
HAL_UART_Transmit_IT / HAL_UART_Receive_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_UART_IRQHandler
end of process callback
HAL_UART_TxCpltCallback
HAL_UART_RxCpltCallback
process Error callback
HAL_UART_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
USART1_IRQHandler
2.1.2

## Slide 31: Use UART with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For transmit use function
  HAL_UART_Transmit_IT(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
For receive use function
  HAL_UART_Receive_IT(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
2.1.2

## Slide 32: Use UART with interrupt
Buffer definition
Sending and receiving methods
/* USER CODE BEGIN 0 */
uint8_t tx_buff[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buff[10];
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_UART_Receive_IT(&huart1,rx_buff,10);
HAL_UART_Transmit_IT(&huart1,tx_buff,10);
/* USER CODE END 2 */
2.1.2

## Slide 33: Use UART with interrupt
Complete callback check
  We can put brakepoints on NOPs to watch if we send or receive complete buffer
/* USER CODE BEGIN 4 */
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart)
{
__NOP();//test if we reach this position
}
void HAL_UART_TxCpltCallback(UART_HandleTypeDef *huart)
{
__NOP();//test if we reach this position
}
/* USER CODE END 4 */
2.1.2

## Slide 34: 2.1.3 UART DMA lab

## Slide 35: Use UART with DMA transfer
Objective
  Learn how to setup UART with DMA in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with DMA
Goal
  Configure UART in CubeMX and Generate Code
  Learn how to send and receive data over UART with DMA
  Verify the correct functionality
2.1.3

## Slide 36: Use UART with DMA transfer
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Pin selection
  It will be same as previous lab we use again PA9 and PA10
2.1.3

## Slide 37: Use UART with DMA transfer
Hardware preparation
  We connect selected pins together by jumper, this help us to create loopback on UART
Hardware loopback
2.1.3

## Slide 38: Use UART with DMA transfer
In order to run on maximum frequency, setup clock system
Details in lab 0
2.1.3

## Slide 39: Use UART with DMA transfer
CubeMX UART configuration
  Tab>Configuration>Connectivity>USART1
2.1.3

## Slide 40: Use UART with DMA transfer
CubeMX USART configuration check:
  BaudRate
  World length
  Parity
  Stop bits
  Data direction
  Oversampling
2.1.3

## Slide 41: Use UART with DMA transfer
CubeMX USART configuration DMA settings
  TAB>DMA Settings
  Button ADD
2.1.3

## Slide 42: Use UART with DMA transfer
CubeMX USART configuration DMA Tx settings
  Set USART1_TX request
  Memory to peripheral direction
  Normal mode
  Byte data width
  Increment memory address
2.1.3

## Slide 43: Use UART with DMA transfer
CubeMX USART configuration DMA Rx settings
  Button ADD
  Set USART1_RX request
  Peripheral to memory direction
  Normal mode
  Byte data width
  Increment memory address
2.1.3

## Slide 44: Use UART with DMA transfer
CubeMX USART configuration NVIC settings
  TAB>NVIC Settings
  Enable DMA2 interrupts for USART1
  Button OK
2.1.3

## Slide 45: Use UART with DMA transfer
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.1.3

## Slide 46: Use UART with DMA transfer
HAL Library UART with DMA RX flow
Start process with DMA end of transfer interrupt generation at end of process
HAL_UART_Receive_DMA
Peripheral Initializations
including DMA stream initializations
HAL_DMA_IRQHandler
end of process callback
HAL_UART_RxCpltCallback
DMA_Stream_IRQHandler
process Error callback
HAL_UART_ErrorCallback
HAL_OK
HAL_ERROR
HAL_ERROR
2.1.3

## Slide 47: Use UART with DMA transfer
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For transmit use function
  HAL_UART_Transmit_DMA(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
For receive use function
  HAL_UART_Receive_DMA(UART_HandleTypeDef *huart, uint8_t *pData, uint16_t Size);
2.1.3

## Slide 48: Use UART with DMA transfer
Buffer definition
Sending and receiving methods with DMA
/* USER CODE BEGIN 0 */
uint8_t tx_buff[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buff[10];
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_UART_Receive_DMA(&huart1,rx_buff,10);
HAL_UART_Transmit_DMA(&huart1,tx_buff,10);
/* USER CODE END 2 */
2.1.3

## Slide 49: Use UART with DMA transfer
Complete callback check
  We can put breakpoints on NOPs to watch if we receive complete buffer
/* USER CODE BEGIN 4 */
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart)
{
__NOP();//check if we receive all data
}
/* USER CODE END 4 */
2.1.3

## Slide 50: 2.2.1 SPI Poll lab

## Slide 51: Simple SPI communication
Objective
  Learn how to setup SPI in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure SPI in CubeMX and Generate Code
  Learn how to send and receive data over SPI without interrupts
  Verify the correct functionality
2.2.1

## Slide 52: Simple SPI communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Pin selection
  We are looking for free pins where is possible to create wire loopback connection
2.2.1

## Slide 53: Simple SPI communication
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX SPI selection
  Select SPI1 Full-Duplex Master
  Select PA5, PA6, PA7 for SPI1 if weren't selected
2.2.1

## Slide 54: Simple SPI communication
Hardware preparation
  Connect PA6 and PA7 together with jumper
Hardware loopback
2.2.1

## Slide 55: Simple SPI communication
In order to run on maximum frequency, setup clock system
Details in lab 0
2.2.1

## Slide 56: Simple SPI communication
CubeMX SPI configuration
  Tab>Configuration>Connectivity>SPI1
  Check the settings
  Button OK
  The CLK frequency with core on 180MHz is now 45MHz
  For this clock use HIGH GPIO speed
2.2.1

## Slide 57: Simple SPI communication
CubeMX SPI – GPIO configuration
  The SPI CLK frequency with core on 180MHz is now 45MHz
  For this clock use HIGH GPIO speed
  Tab>Configuration>System> >GPIO
  Tab>SPI1
  Seth High output speed
  Button OK
2.2.1

## Slide 58: Simple SPI communication
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.2.1

## Slide 59: Simple SPI communication
HAL Library transmit receive flow
HAL_TIMEOUT
HAL_ERROR
HAL_OK
Function blocks
Polling with timeout
Peripheral Initializations
Polling process
HAL_SPI_TransmitReceive
HAL_BUSY
2.2.1

## Slide 60: Simple SPI communication
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
For transmit and receive use function
  HAL_SPI_TransmitReceive(SPI_HandleTypeDef *hspi, uint8_t *pTxData, uint8_t *pRxData, uint16_t Size, uint32_t Timeout)
2.2.1

## Slide 61: Simple SPI communication
Transmit receive solution
  Create data structure for data
  Call transmit receive function
/* USER CODE BEGIN PV */
uint8_t tx_buffer[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buffer[10];
/* USER CODE END PV */
/* USER CODE BEGIN 2 */
HAL_SPI_TransmitReceive(&hspi1,tx_buffer,rx_buffer,10,100);
/* USER CODE END 2 */
2.2.1

## Slide 62: 2.2.2 SPI Interrupt lab

## Slide 63: Use SPI with interrupt
Objective
  Learn how to setup SPI with interrupts in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Create simple loopback example with interrupts
Goal
  Configure SPI in CubeMX and Generate Code
  Learn how to send and receive data over SPI with interrupts
  Verify the correct functionality
2.2.2

## Slide 64: Use SPI with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX SPI selection
  Select SPI1 Full-Duplex Master
  Select PA5, PA6, PA7 for SPI1 if weren't selected
2.2.2

## Slide 65: Use SPI with interrupt
Hardware preparation
  Connect PA6 and PA7 together with jumper
Hardware loopback
2.2.2

## Slide 66: Use SPI with interrupt
In order to run on maximum frequency, setup clock system
Details in lab 0
2.2.2

## Slide 67: Use SPI with interrupt
CubeMX SPI configuration
  Tab>Configuration>Connectivity>SPI1
  Check the settings
  Button OK
2.2.2

## Slide 68: Use SPI with interrupt
CubeMX SPI configuration
  TAB>NVIC Settings
  Enable SPI interrupt
  Button OK
2.2.2

## Slide 69: Use SPI with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
2.2.2

## Slide 70: Use SPI with interrupt
HAL Library SPI with IT transmit receive flow
Start process with interrupt generation at end of process
HAL_SPI_TransmitReceive_IT
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_SPI_IRQHandler
end of process callback
HAL_SPI_TxRxCpltCallback
process Error callback
HAL_SPI_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
SPI1_IRQHandler
2.2.2

## Slide 71: Use SPI with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For transmit use function
  HAL_SPI_TransmitReceive_IT(SPI_HandleTypeDef *hspi, uint8_t *pTxData, uint8_t *pRxData, uint16_t Size)
2.2.2

## Slide 72: Use SPI with interrupt
Buffer definition
Sending and receiving methods
/* USER CODE BEGIN 0 */
uint8_t tx_buff[]={0,1,2,3,4,5,6,7,8,9};
uint8_t rx_buff[10];
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_SPI_TransmitReceive_IT(&hspi1,tx_buff,rx_buff,10);
/* USER CODE END 2 */
2.2.2

## Slide 73: Use SPI with interrupt
Complete callback check
  We can put breakpoints on NOPs to watch if we send or receive complete buffer
/* USER CODE BEGIN 4 */
void HAL_SPI_TxRxCpltCallback(SPI_HandleTypeDef *hspi)
{
__NOP();
}
/* USER CODE END 4 */
2.2.2

## Slide 74: 3.2.1 TIM with interrupt lab

## Slide 75: Use TIM with interrupt
Objective
  Learn how to setup TIM with Interrupt in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Indicate TIM interrupt with LED toggle
Goal
  Configure TIM in CubeMX and Generate Code
  Learn how start timer and handle interrupt
  Verify the correct functionality
3.2.1

## Slide 76: Use TIM with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX TIM selection
  Select TIM clock source Internal clock
  Enable GPIO for LED PG14
3.2.1

## Slide 77: Use TIM with interrupt
CubeMX TIM configuration
  Tab>Configuration>Control>TIM1
  Check the settings
3.2.1

## Slide 78: Use TIM with interrupt
CubeMX TIM configuration
  Tab>Parameter Settings
  Prescaler to 18000
  Counter period to 10000
  Together with 180MHz TIMER1 clock we get period 1Hz
3.2.1

## Slide 79: Use TIM with interrupt
CubeMX TIM configuration
  Tab>NVIC Settings
  Enable TIM1 Update interrupt
  Button OK
3.2.1

## Slide 80: Use TIM with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
3.2.1

## Slide 81: Use TIM with interrupt
HAL Library TIM with IT flow
Start process with interrupt generation at end of process
HAL_TIM_Base_Start_IT
TIM Initializations
including peripheral interrupt NVIC initializations
HAL_TIM_IRQHandler
process callback
HAL_TIM_PeriodElapsedCallback
process Error callback
HAL_TIM_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
TIM1_UP_TIM10_IRQHandler
3.2.1

## Slide 82: Use TIM with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For TIM start use function
  HAL_TIM_Base_Start_IT(TIM_HandleTypeDef *htim)
TIM callback
  void TIM1_UP_TIM10_IRQHandler(void)
GPIO LED toggle
  HAL_GPIO_TogglePin(GPIO_TypeDef* GPIOx, uint16_t GPIO_Pin)
3.2.1

## Slide 83: Use TIM with interrupt
Solution
  TIM start
  Callback handling
/* USER CODE BEGIN 2 */
HAL_TIM_Base_Start_IT(&htim1);
/* USER CODE END 2 */
/* USER CODE BEGIN 4 */
void HAL_TIM_PeriodElapsedCallback(TIM_HandleTypeDef *htim)
{
HAL_GPIO_TogglePin(GPIOG,GPIO_PIN_14);
}
/* USER CODE END 4 */
3.2.1

## Slide 84: 3.2.2 TIM with PWM output lab

## Slide 85: Use TIM with PWM output
Objective
  Learn how to setup TIM with PWM out in CubeMX
  How to Generate Code in CubeMX and use HAL functions
  Indicate TIM PWM on LED
Goal
  Configure TIM in CubeMX and Generate Code
  Learn how start timer and set PWM out
  Verify the correct functionality with LED
3.2.2

## Slide 86: Use TIM with PWM output
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX TIM selection
  Select TIM clock source - Internal clock
  Set Channel1 to PWM generation
3.2.2

## Slide 87: Use TIM with PWM output
CubeMX TIM configuration
  TAB>Configuration >Control>TIM1
  TAB>Parameter settings
  Prescaler to 18000
  Counter period to 10000
  Together with 180MHz TIMER1 clock we get period 1Hz
  PWM pulse to 5000 this give us 1Hz blinking frequency
3.2.2

## Slide 88: Use TIM with PWM output
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
3.2.2

## Slide 89: Use TIM with PWM output
Start process TIM with PWM(same for DMA, ADC)
  Non blocking start process
Peripheral Initializations
Start Process
HAL_TIM_PWM_Start
3.2.2

## Slide 90: Use TIM with PWM output
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
For TIM start use function
  HAL_TIM_PWM_Start(TIM_HandleTypeDef *htim, uint32_t Channel)
GPIO LED toggle
  We wire the Channel1 PE9 with LED PG14
3.2.2

## Slide 91: Use TIM with PWM output
Solution
  TIM PWM start
  TIM1 Channel 1 and LED connection
/* USER CODE BEGIN 2 */
HAL_TIM_PWM_Start(&htim1,TIM_CHANNEL_1);
/* USER CODE END 2 */
3.2.2

## Slide 92: www.st.com/stm32